## Slide 3
Find components
Is found components ripples? [profiling]
What is the orientation of found components? A cluster of ripples has roughly the same angle [histogram analysis]

## Slide 4: (1) Find components
OPENCV connectedComponents
  Find all components (of shadows)
  Each component
    Known as drawings/masks in source code

## Slide 5: (2) Is found components ripples?
Get profiles of each component
  Draw lines (profile lines)
  Get component pixels under profile lines
  Rules to inspect profiles:
    Plot profiles and compare them
      Will see the shape of component
        Tapers down at the ends with bulge in middle
    find average profile
      will suppress noise &
      emphasize bulge
  Rules must help reject or accept component as ripple

## Slide 6: (3) What is the orientation of found components?
Once component is found:
  Create bins of 5 degrees wide
  Pack all angles in bins
  Pack corresponding original image pixels in bins
    Find bin with the most (max)samples (pixels) in it (let’s say it is bin 70-75)
    Find centre of bin – this is dominant angle – angle of bin – angle of all the pixels inside bin
    Colour bin’s pixels & plot them back onto image/edge
    Does plotted coloured pixels give components entire edge?
    If not, pack a bin on either side of max bin and repeat from (a)
    If yes, this bin’s orientation is the discovered dominant angle
    Repeat for all bins

## Slide 7
For (each component)
  Profile component
    Generate profiles of component
    Does component have ripple shape?
      Starting from one end of component, does number of component pixels increase as you move closer to centre of component, & then starts tapering down again?
  Histogram analyse component
    Find component angle
    Does component have angle similar to other components?